## Slide 1
Lecture 1 Introduction
School of Computer Engineering and Science
Shanghai University
Instructor: Jianjia Wang, Shengyu Duan

## Slide 2: Outline: Lecture 1: Introduction
Preliminary
What are the signals
What are the systems
Application of signals and systems
Fundamental concepts
Types of Signals

## Slide 3: Outline: Lecture 1: Introduction
Preliminary
What are the signals
What are the systems
Application of signals and systems
Fundamental concepts
Types of Signals

## Slide 4: 信号是什么？
烽火狼烟
电话
无线电
物联网

## Slide 5: What is a Signal?
A signal is a pattern of variation of some form
Signals are variables that carry information
Any kind of physical variable subject to variations represents a signal
Examples of signal include:
  Electrical signals
          Voltages and currents in a circuit
  Acoustic signals
          Acoustic pressure (sound) over time
  Mechanical signals
          Velocity of a car over time
  Video signals
          Intensity level of a pixel (camera, video) over time
Notes: 信号=模式（信息）+变量（物理）

## Slide 6: How is a Signal Represented?
Mathematically, signals are represented as a function of one or more independent variables.
For instance a black & white video signal intensity is dependent on x, y coordinates and time t f(x,y,t)
On this course, we shall be exclusively concerned with signals that are a function of a single variable: time
t
f(t)

## Slide 7: How is a Signal Represented?
A signal is a set of information of data
  Both the independent variable and the physical variable can be either scalars or vectors
    Independent variable: time (t), space (x, x=[x1,x2], x=[x1,x2,x3])
    Signal:
    Electrochardiography signal (EEG) 1D, voice 1D, music 1D
    Images (2D), video sequences (2D+time), volumetric data (3D)

## Slide 8: Example: 1D biological signals: ECG
amplitude
time

## Slide 9: Example: 2D biological signals: MI
MRI
CT
US

## Slide 10: Example : Natural image

## Slide 11: Signals as functions
Continuous functions of real independent variables
– 1D: f=f(x)
  2D: f=f(x,y) x,y
  Real world signals (audio, ECG, images)
Real valued functions of discrete variables
– 1D: f=f[k]
– 2D: f=f[i,j]
  Sampled signals
Discrete functions of discrete variables
  1D: fd=fd[k]
  2D: fd=fd[i,j]
  Sampled and quantized signals
Gray scale images: 2D functions
  Domain of the functions: set of (x,y) values for which f(x,y) is defined : 2D lattice
[i,j] defining the pixel locations
  Set of values taken by the function : gray levels
Digital images can be seen as functions defined over a discrete domain {i,j: 0<i<I, 0<j<J}
I,J: number of rows (columns) of the matrix corresponding to the image
f=f[i,j]: gray level in position [i,j]

## Slide 12: Example : function

0
i  j  0
i, j  0;i  j
 i, j 1

0
i  0; j  J otherwise
 i, j  J  1
1
2 2
 2
e
x2  y2
f (x, y) 
1
 2
e 2 2
i2  j 2
f [i, j] 
Continuous function
Discrete version

## Slide 13: Continuous & Discrete-Time Signals
Continuous-Time Signals
Most signals in the real world are continuous time, as the scale is infinitesimally fine.
E.g. voltage, velocity,
Denote by x(t), where the time interval may be bounded (finite) or infinite
Discrete-Time Signals
Some real world and many digital signals are discrete time, as they are sampled
E.g. pixels, daily stock price (anything that a digital computer processes)
Denote by x[n], where n is an integer value that varies discretely
Sampled continuous signal
x[n] =x(nk) – k is sample time
x(t)
t
x[n]
n

## Slide 14: 连续时间与离散时间信号
对连续时间信号x(t)， t可以是任意值（无限个数的值）；
对离散时间信号x[n]， n为有限个数的值；
x(t)
t
x[n]
n

## Slide 15: 连续时间与离散时间信号
对连续时间信号x(t)， t可以是任意值（无限个数的值）；
对离散时间信号x[n]， n为有限个数的值；
然而，连续与离散信号真的可以明确划分吗？
x(t)
t
x[n]
n

## Slide 16: 连续时间与离散时间信号
对以下连续时间信号x(t)，不断拉近
对以下离散时间信号x[n]，将n与n+1之间的间隔不断缩小
“连续”与“离散”存在主观性：连续信号是间隔无限接近于0的离散信号。
上述概念帮助理解不同信号类型的傅里叶变化及采样（连续/离散时间信号无法明确划分，但有必要去划分）。

## Slide 17: Continuous & Discrete-Time Signals
Time signals:
Continuous time signals (analog signals): for example, audio signals (FMsignals), AC voltages and currents
Discrete time signals (digital signals): for example, daily temperature
Note that continuous time signals and discrete time signals can be converted to each other.

## Slide 18: Continuous & Discrete-Time Signals
1D signal (e.g., voice, music): x(t) -> x[n]
2D signal (e.g., images): x(s1,s2) → x[n1,n2]
2D signal (e.g., videos: 2D spatial + time): x(s1,s2,t) → x[n1,n2,n]

## Slide 19: Signal Properties
On this course, we shall be particularly interested in signals with certain properties:
Periodic signals: a signal is periodic if it repeats itself after a fixed period T, i.e. x(t) = x(t+T) for all t. A sin(t) signal is periodic.
Even and odd signals: a signal is even if x(-t) = x(t) (i.e. it can be reflected in the axis at zero). A signal is odd if x(-t) = -x(t). Examples are cos(t) and sin(t) signals, respectively.
Exponential and sinusoidal signals: a signal is (real) exponential if it can be represented as x(t) = Ceat. A signal is (complex) exponential if it can be represented in the same form but C and a are complex numbers.
Step and pulse signals: A pulse signal is one which is nearly completely zero, apart from a short spike, d(t). A step signal is zero up to a certain time, and then a constant value after that time, u(t).
These properties define a large class of tractable, useful signals and will be further considered in the coming lectures
Notes: Pulse signal: 冲激信号
Step signal：阶跃信号

## Slide 20: What is a System?
Systems process input signals to produce output signals
Examples:
  A circuit involving a capacitor can be viewed as a system that transforms the
  source voltage (signal) to the voltage (signal) across the capacitor
  A CD player takes the signal on the CD and transforms it into a signal sent to
  the loud speaker
System
input
output
The function linking the output of the system with the input signal is called transfer function and it is typically indicated with the symbol h(•)
Circuit:
Notes: Transfer function：传递函数

## Slide 21: What is a System?
  A communication system is generally composed of three sub-systems, the transmitter, the channel and the receiver. The channel typically attenuates and adds noise to the transmitted signal which must be processed by the receiver
Communication Systems
Transmitter
Receiver
Channel
Transmitted signal
noise, loss
distortion,
interference
Received signal
Estimate of message signal (information)
Message signal (information) data, text, audio, video
r(t)
s(t)

## Slide 22: How is a system Represented?
A system takes a signal as an input and transforms it into another signal
In a very broad sense, a system can be represented as the ratio of the output signal over the input signal
System
Input signal
x(t)
Output signal
y(t)
  That way, when we “multiply” the system by the input signal, we get the output signal
  This concept will be firmed up in the coming weeks

## Slide 23: 系统
系统往往是以一定比例（做乘法）放大、缩小输入信号
例如：幅度调制（Amplitude Modulation，AM）
System
Input signal
x(t)
Output signal
y(t)

## Slide 24: Continuous & Discrete-Time Mathematical Models of Systems
Continuous-Time Systems
Most continuous time systems represent how continuous signals are transformed via differential equations.
E.g. circuit, car velocity
Discrete-Time Systems
Most discrete time systems represent how discrete signals are transformed via difference equations
E.g. bank account, discrete car velocity system
First order differential equations
First order difference equations

## Slide 25: Properties of a System
On this course, we shall be particularly interested in signals with certain properties:
Causal: a system is causal if the output at a time, only depends on input values up to that time.
Linear: a system is linear if the output of the scaled sum of two input signals is the equivalent scaled sum of outputs
Time-invariant: a system is time invariant if the system’s output is the same, given the same input signal, regardless of time.
These properties define a large class of tractable, useful systems and will be further considered in the coming lectures
Notes: Causal：具有因果性的

## Slide 26: 系统的因果性（Causality）
Causal: a system is causal if the output at a time, only depends on input values up to that time. （系统的输出只取决于现在的输入及过去的输入）
具有因果性的系统才是物理可实现的系统
因果性的意义：判断所设计的系统是否是可以被实现的
例：理想低通滤波器不具有因果性，是不可能被实现的

## Slide 27: 线性（Linear）系统
Linear: a system is linear if the output of the scaled sum of two input signals is the equivalent scaled sum of outputs （如果输入信号是两个信号的加权和，那么输出信号也是这两个输入信号对应输出的加权和）
例：如果系统对输入信号x(t)的输出是y(t)，则系统对输入信号ax1(t)+bx2(t)的输出为ay1(t)+by2(t)
线性系统对信号在频域表示下的处理具有重要意义。

## Slide 28: 时不变（Time-invariant）系统
Time-invariant: a system is time invariant if the system’s output is the same, given the same input signal, regardless of time. （系统特性不随时间发生变化）
例：如果系统对输入信号x(t)的输出是y(t)，则系统对输入信号x(t-t0)的输出为y(t-t0)
时不变系统对信号在频域表示下的处理具有重要意义。

## Slide 29: Typical Examples of Signals/Systems Concerned
Computers
Signal Processing Systems
    software systems processing the signal by computation/ memory
    examples : audio enhancement systems, picture processing systems, video compression systems, voice recognition/ synthesis systems, array signal processors, equalizers, etc.

## Slide 30: Typical Examples of Signals/Systems Concerned
Networks
user A
user B

## Slide 31: Typical Examples of Signals/Systems Concerned
Information Retrieval Systems
Internet
Other Information Systems
    examples : remote sensing systems, biomedical signal
    processing systems, etc.
Search Engine
Internet
User

## Slide 32: Internet
Internet
Digital
Libraries,
Virtual
Museums,
.
.
.
Electronic
Commerce,
Network
Banking,
.
.
.
Electronic
Government
Services,
.
.
.
Intelligent
Offices,
Distant
Learning,
.
.
.
Electronic
Home,
Network
Entertainment
.
.
.
Google,
Facebook,
YouTube,
Amazon
.
.
.

## Slide 33: Internet
Network Technology Connects Everywhere Globally
Huge Volume of Information Disseminated across the Globe in Microseconds
Multi-media, Multi-lingual, Multi-functionality
Cross-cultures, Cross-domains, Cross-regions
Integrating All Knowledge Systems and Information related Activities Globally

## Slide 34: Typical Examples of Signals/Systems Concerned
Control Systems
    close-loop/feedback control systems
    example: aircraft landing systems, satellite stabilization systems, robot arm control systems, etc.
plant
controller
error signal e(t)
sensor
control signal v(t)
output signal y(t)
input signal x(t)
disturbance z(t)
feedback signal

## Slide 35: Typical Examples of Signals/Systems Concerned
Other Systems
    manufacturing systems, computer-aided-design systems, mechanical systems, chemical process systems, etc.

## Slide 36: 信号处理与人工智能
例：实现一个简单的声音识别系统，对发声者的年龄、性别进行判断

## Slide 37: 信号处理与人工智能
例：实现一个简单的声音识别系统，对发声者的年龄、性别进行判断
以人工神经网络构建分类器：
  每一层网络提取信号中的抽象特征

## Slide 38: 信号处理与人工智能
例：实现一个简单的声音识别系统，对发声者的年龄、性别进行判断
以人工神经网络构建分类器：
  每一层网络提取信号中的抽象特征
以传统信号处理技术构建系统：
  提取信号中频率特征

## Slide 39: 信号处理与人工智能
广义上来说，人工智能是抽象层面下的信号处理，以通过提取目前人类无法解释的特征来处理信号
信号处理可以是一种可解释的人工智能架构
信号处理与人工智能在未来的某一天是否会完全融合？
信号处理
人工智能

## Slide 40: Outline: Lecture 1: Introduction
Preliminary
What are the signals
What are the systems
Application of signals and systems
Fundamental concepts
Types of Signals

## Slide 41: Classification of signals
Continuous time – Discrete time
Analog – Digital (numerical)
Periodic – Aperiodic
Energy – Power
Deterministic – Random (probabilistic)
Note
  Such classes are not disjoint, so there are digital signals that are periodic of power type and others that are aperiodic of power type etc.
  Any combination of single features from the different classes is possible

## Slide 42: Continuous time – discrete time
Continuous time signal: a signal that is specified for every real value of the independent variable
  The independent variable is continuous, that is it takes any value on the real axis
  E.g. The domain of the function representing the signal has the cardinality of real numbers
Signal ↔ f=f(t)
Independent variable ↔ time (t), position (x)
For continuous-time signals:
t  ℝ
time
amplitude

## Slide 43: Continuous time – discrete time
Discrete time signal: a signal that is specified only for discrete values of the independent variable
  It is usually generated by sampling so it will only have values at equally spaced
intervals along the time axis
  E.g. The domain of the function representing the signal has the cardinality of integer numbers
Signal ↔ f=f[n], also called “sequence”
Independent variable ↔ n
For discrete-time functions: t  Z
time (discrete)
amplitude

## Slide 44: Analog - Digital
Analog signal: signal whose amplitude can take on any value in a continuous range
  The amplitude of the function f(t) (or f(x)) has the cardinality of real numbers
    The difference between analog and digital is similar to the difference between continuous-time and discrete-time. In this case, however, the difference is with respect to the value of the function (y-axis)
  Analog corresponds to a continuous y-axis, while digital corresponds to a discrete y-axis
Here we call digital what we have called quantized in the EI class
An analog signal can be both continuous time and discrete time

## Slide 45: Analog - Digital
Digital signal: a signal is one whose amplitude can take on only a finite number of values (thus it is quantized)
  The amplitude of the function f() can take only a finite number of values
  A digital signal whose amplitude can take only M different values is said to be Mary
    Binary signals are a special case for M=2
time
amplitude

## Slide 46: Example
– Continuous time analog
time
Continuous time digital (or quantized)
  binary sequence, where the values of the function can only be one or zero.
amplitude
time
amplitude
Discrete time analog
Discrete time digital
  binary sequence, where the values of the function can only be one or zero.
time
amplitude
time
amplitude

## Slide 47: Summary
Signal amplitude/ Time or space | Real | Integer
Real | Analog Continuous-time | Digital Continuous-time
Integer | Analog Discrete-time | Digital Discrete time

## Slide 48: Periodic - Aperiodic
A signal f(t) is periodic if there exists a positive constant T0 such that
f (t  T0 )  f (t) t
  The smallest value of T0 which satisfies such relation is said the period of the function f(t)
  A periodic signal remains unchanged when time-shifted of integer multiples of the period
  Therefore, by definition, it starts at minus infinity and lasts forever
  t   t  °
  n   n  Z
  Periodic signals can be generated by periodical extension

## Slide 49: Examples
Periodic signal with period T0
Aperiodic signal
Notes: 周期与非周期具有主观性

## Slide 50: Examples
Periodic signal with period T0
Still an aperiodic signal?
周期与非周期性同样具有主观性！
Notes: 周期与非周期具有主观性

## Slide 51: Causal and non-Causal signals
Causal signals are signals that are zero for all negative time (or spatial positions), while
Anticausal are signals that are zero for all positive time (or spatial positions).
Noncausal signals are signals that have nonzero values in both positive and negative time
Notes: 区别系统的因果性与信号的因果性
因果系统：输出取决于当前及以前的输入
因果信号：时间原点之后才产生的信号

## Slide 52: Causal and non-causal signals
Causal signals
f (t)  0 t  0
Anticausals signals
f (t)  0 t  0
Non-causal signals
t1  0:
f (t1 )  0

## Slide 53: Even and Odd signals
An even signal is any signal f such that f (t) = f (-t). Even signals can be easily spotted as they are symmetric around the vertical axis.
An odd signal, on the other hand, is a signal f such that f (t)= - (f (-t))

## Slide 54: Decomposition in even and odd components
Any signal can be written as a combination of an even and an odd signals
– Even and odd components
 
   
 
   
 
2
1
2
1
2
e
o  
f
f
f t   1  f t   f t   1  f t   f t 
f t 
2
t  f t even component
f t 
t  f t odd component
f t   fe t   fo t 
重要！

## Slide 55: Example

## Slide 56: Example
Proof

## Slide 57: Some properties of even and odd functions
even function x odd function = odd function
odd function x odd function = even function
even function x even function = even function
Area
a a
 a 0
a
 a
 fe t  dt  2 fe t dt
 fe t  dt  0

## Slide 58: Deterministic - Probabilistic
Deterministic signal: a signal whose physical description in known completely
A deterministic signal is a signal in which each value of the signal is fixed and can be determined by a mathematical expression, rule, or table.
Because of this the future values of the signal can be calculated from past values with complete confidence.
  There is no uncertainty about its amplitude values
  Examples: signals defined through a mathematical function or graph
Probabilistic (or random) signals: the amplitude values cannot be predicted precisely but are known only in terms of probabilistic descriptors
The future values of a random signal cannot be accurately predicted and can usually only be guessed based on the averages of sets of signals
  They are realization of a stochastic process for which a model could be available
  Examples: EEG, evocated potentials, noise in CCD capture devices for digital cameras

## Slide 59: Example
Deterministic signal
Random signal
time
amplitude
amplitude
time

## Slide 60: Finite and Infinite length signals
An infinite length signal is non zero over an infinite set of values of the independent variable
– For instance, a sinusoid f(t)=sin(ωt) is an infinite length signal
A finite length signal is non-zero over a finite set of values of the independent variable
f  f t , t : t1  t  t2 t1  , t2  

## Slide 61: Size of a signal: Norms
"Size" indicates largeness or strength.
We will use the mathematical concept of the norm to quantify this notion for both continuous-time and discrete-time signals.
The energy is represented by the area under the curve (of the squared signal)
time
amplitude
0
T
Notes: Norm：范数，空间中的长度

## Slide 62
Energy
Signal energy
f
f
f 2 (t)dt
f (t) 2 dt

Generalized energy : Lp norm
– For p=2 we get the energy (L2 norm)
E 
E 





 
 
 


1/ p
p
f t
f t
dt

1  p  


## Slide 63: Power
Power
– The power is the time average (mean) of the squared signal amplitude, that is the
mean-squared value of f(t)
2
1
1
f
f 2 (t)dt
f (t) dt
T /2
T  T
T /2
T /2
T 
T /2
P  lim
Pf  lim T



## Slide 64: Power - Energy
The square root of the power is the root mean square (rms) value
  This is a very important quantity as it is the most widespread measure of similarity/dissimilarity among signals
  It is the basis for the definition of the Signal to Noise Ratio (SNR)
– It is such that a constant signal whose amplitude is =rms holds the same power content of the signal itself
There exist signals for which neither the energy nor the power are finite
t
f
ramp
0
noise
P

Psignal 
SNR  20log
10 

 
Notes: RMSE：均方根误差

## Slide 65: Energy and Power signals
A signal with finite energy is an energy signal
  Necessary condition for a signal to be of energy type is that the amplitude goes to zero as the independent variable tends to infinity
A signal with finite and different from zero power is a power signal
  The mean of an entity averaged over an infinite interval exists if either the entity is periodic or it has some statistical regularity
  A power signal has infinite energy and an energy signal has zero power
  There exist signals that are neither power nor energy, such as the ramp
All practical signals have finite energy and thus are energy signals
  It is impossible to generate a real power signal because this would have infinite duration and infinite energy, which is not doable.
Notes: 有限能量的信号，其功率一定为0。因此，在无穷大的区间计算功率，意义不大。实际更多的是，在有限的时间区间内（如一个周期内），计算功率。

## Slide 66: Useful signal operations: shifting, scaling, inversion
Shifting: consider a signal f(t) and the same signal delayed/anticipated by T
seconds
f(t)
t
f(t+T)
t
t
T
f(t-T)
T
T>0
anticipated
delayed

## Slide 67: Useful signal operations: shifting, scaling, inversion
(Time) Scaling: compression or expansion of a signal in time
f(t)
t
f(2t)
t
f(t/2)
compression
 t   f 2t 
expansion  t   f t / 2
t

## Slide 68: Useful signal operations: shifting, scaling, inversion
Scaling: generalization
a  1
 t   f at 
 compressed version
 t   f  t   dilated (or expanded) version
 a 
 
Viceversa for a  1

## Slide 69: Useful signal operations: shifting, scaling, inversion
(Time) inversion: mirror image of f(t) about the vertical axis
 t   f t 
f(t)
f(-t)
0
0

## Slide 70: Useful signal operations: shifting, scaling, inversion
Combined operations: f(t) → f(at-b)
Two possible sequences of operations
Time shift f(t) by to obtain f(t-b). Now time scale the shifted signal f(t-b) by a to obtain f(at-b).
Time scale f(t) by a to obtain f(at). Now time shift f(at) by b/a to obtain f(at-b).
  Note that you have to replace t by (t-b/a) to obtain f(at-b) from f(at) when replacing t by the translated argument (namely t-b/a))

## Slide 71: Outline: Lecture 1: Introduction
Preliminary
What are the signals
What are the systems
Application of signals and systems
Fundamental concepts
Types of Signals

## Slide 72: Useful functions
Unit step function （单位阶跃函数）
– Useful for representing causal signals
u t   1
0
t  0
t  0

f t   u t  2  u t  4
Continuous and discrete time unit step functions
u(t)
u[k]

## Slide 73: Useful functions
Ramp function (continuous time)
Notes: Ramp signal：斜坡函数

## Slide 74: Useful functions
Unit impulse function （单位冲激函数）
 t   0
t  0

  t  dt  1

t
0
t
 |  | ε→0 | 
1/ ε |  |  | 
 t 
1
0
e
Notes: 单位冲激函数面积为1

## Slide 75: Properties of the unit impulse function
– The area under the curve obtained by the product of the unit impulse function shifted by T and (t) is the value of the function (t) for t=T
Multiplication of a function by impulse
 t  t    0 t 
 t  t  T    T  t  T 
Sampling property of the unit function
 

  

  t  t  dt    0 t dt   0   t dt   0
  t  t  T  dt   T 


## Slide 76
Properties of the unit impulse function
The unit step function is the integral of the unit impulse function
– Thus
du
dt   t 
t
  t dt  u t 

t

0 t  0
t  0

  t  dt  u t   1

## Slide 77: Properties of the unit impulse function
Discrete time impulse function

## Slide 78: Unit Impulse and Unit Step Functions
  Discrete-time
      First difference
      Running Sum
      Sampling property

## Slide 79: Unit Impulse & Unit Step
  Discrete-time
δ [n] = u[n] – u[n – 1]
n
n
n
δ [n]
u [n]
u [n – 1]

## Slide 80: Useful functions
Discrete time complex exponential
– k=nT
Continuous time complex exponential
f t   Ae jt
Euler’s relations

## Slide 81: Useful functions
Exponential function est
– Generalization of the function ejωt
s    j

## Slide 82: The exponential function
s=σ
s=jω
s    j
s    j

## Slide 83: The exponential function
s=σ
s=jω
s    j
s    j
σ
left half plan exponentially decreasing signals
right half plan exponentially increasing signals
signals of constant amplitude
jω
monotonically increasing/decreasing exponentials

## Slide 84: 本章部分关键词汇中英文对照表
离散时间信号 | Discrete-time signal
连续时间信号 | Continuous-time signal
指数信号 | Exponential signal
正弦信号 | Sinusoidal signal
余弦信号 | Cosinusoidal signal
阶跃函数 | Step function
冲激函数 | Impulse signal
斜坡函数 | Ramp signal
因果系统 | Casual system
模拟信号 | Analog signal
数字信号 | Digital signal
复数 | Complex number
实数 | Real number
虚数 | Imaginary number

## Slide 85
Thank you for your listening!